## Slide 1: The Ideal Washeteria for Large Population, Highly Dependent
Group 3

## Slide 2: Initial Approach
Examine current practice: data on current facility (location, use, likes/dislikes, “turns per day”, peak use hours, physical use patterns, etc)
Consider paying someone to gather use information on site
Determine whether water treatment plant will be co-located (assume that it will)
Demographics – population, income, other businesses
Input from community – ideas, brainstorming, multi-use ideas
Options for waste heat, wind, etc.

## Slide 3: Design elements
Size and number of bathrooms and machines will be key consideration on for this facility, given heavy use
Consider separate heating system for dryers in order more energy efficiency and drying time (180 degree operation)
Explore hybrid heating for dryers (electric and fuel fired)
Use waste heat to pre-heat the dryer plenum
Use slab on grade foundation, if possible, to allow concrete floor. Otherwise, consider polyuria as flooring.
Make room for kids to hang out,
Space for other enterprises like food and beverage sales

## Slide 4: Design, continued
Consider including city office in same facility
Include space for attendant, storage, etc.
Consider itinerant lodging
Incorporate ability to add on to building into design – so future funding could construct addition for other uses
(Additional space for the other uses is primarily a capital expense, so capital funding may be a limitation)

## Slide 5: Design (continued)
Modularity: Consider modular design if several facilities are being developed at same time.
Standard equipment and processes (brands, etc.): Promote and use to the extent possible.
Community input into how the building looks and fits in.
Steel siding
Think about “flow” from one washer type to the right type of dryer
Air re-use of dryer air to reduce energy usage
Explore potential for heat recovery from wastewater
Better ventilation could enhance user experience

## Slide 6: Construction
Look at alternatives to local labor force account construction – talk about construction contracts, design/build, etc.
Metal pre-fab structure would probably allow for more multi-use options and open areas.
Work with Cold Climate Housing center on alternative contruction approaches

## Slide 7: Sanitary Facilities: Contribution to Health
Use anti-microbial surfaces wherever possible (copper, silver, etc.)
Consider incorporating ozone into laundry – ensures a “kill step” in laundering process without paying for dryer (needs more information)
Consider pricing for both washers and dryers so customers will user dryers.
Greatly improved O&M manuals and training to improve sanitary conditions

## Slide 8: Economics
Explore partnership with economic enterprise to operate and maintain the washeteria (rather than local government)
Mom and Pop operation – contract with someone local for five years
Create a new cooperative to partner with smaller communities on operation of washeterias (similar to ARUC for piped communities)
Enhanced training programs to approach washeteria operation (and book keeping) as business, rather than government function.
Three keys to economic viability of business approach: pricing, hours, and services

## Slide 9: Economics (continued)
Additional services – wash/dry/fold
Onsite chlorine production for household sales (locally made bleach)
Policy of only allowing detergent sold at facility (none from home) – helps to keep machines from breaking and increases revenue
Appointment times for extra fee or low-use hours
Space rental for birthday parties, meetings, etc.

## Slide 10: Use/User Needs
Additional services will help to make sure an attendant is on duty
Re-name the facility with local input – naming and logo contest that will impart local meaning and purpose
Get sociologist or other expertise involved in early project to help build local buy in (not a job for engineers!)
Use architect to enhance the experience of using the facility, leading to increased use
Closed-circuit camera record for vandalism prevention (all hours)